## Slide 1
NETWORK SUPPORT · PORTFOLIO · VIDEO SERIES
QVIS
QVIS Technology Solutions
A fictional 10-person IT consultancy that has to scale to 20 — and the network I built for them.
Olumide Akomolafe
Network Support Technician · Conestoga College · Cambridge, ON
1 / 23

## Slide 2
EP 01
WHO IS QVIS
A 10-person IT consultancy. Twelve months to 20.
Small, sensitive, growing fast — every design lever pulled accordingly.
EMPLOYEES AT LAUNCH
10
→ 20 within 12 months
CLIENT VERTICALS
4
legal · dental · accounting · manufacturing
COMPLIANCE PRESSURE
SOC 2
client-driven · PIPEDA-aware · PHIPA-adjacent
1.
Headcount small but sensitivity real — SOC 2 expectation from clients on day one
2.
They grow — sizing for 10 means re-IP within the first year (no thanks)
3.
Twelve named rooms on one floor — room layout drives the cabling, not the other way round
QVIS · Olumide Akomolafe · Conestoga Network Support Technician
2 / 23

## Slide 3
EP 01
WHAT THIS PORTFOLIO COVERS
Four episodes. Four facets of a real Tier-1/2 build.
Each one stands alone; together they answer "what would you do on day one?"
01
Meet QVIS
Brief · floor plan · design goals · why each call was made
02
Build it in Packet Tracer
10 VLANs · trunks · inter-VLAN routing on the L3 core · named ACLs
03
Identity and services
AD on Win Server 2022 · function-first OUs · AGDLP · DHCP · DNS · GPOs
04
Troubleshoot like a technician
Three tickets · OSI-shaped triage · root cause · runbook fix
~ 20 minutes total runtime · screencast + voiceover · source repo linked in description
QVIS · Olumide Akomolafe · Conestoga Network Support Technician
3 / 23

## Slide 4
EP 01
THE BRIEF — IN ONE LINE
"Build a network a real Tier-1 or Tier-2 technician
could be hired into on day one."
What that means in practice:
No enterprise gear we wouldn't see in a 10-person office.
No over-engineering for marketing.
Every choice has to survive an audit.
QVIS · Olumide Akomolafe · Conestoga Network Support Technician
4 / 23

## Slide 5
EP 01
FLOOR PLAN & TOPOLOGY PREVIEW
One floor, twelve rooms, two wings, server room in the middle.
The room layout drives the cabling — TIA-568 90-metre run limit is the constraint.
NORTH WING
R1 Reception
R2 Exec office
R3 Finance/HR
R4 Sales bullpen
R8 Conference
R9 Huddle
R11 Break room
SOUTH WING
R5 Tech workstations
R6 NOC
R10 Training Lab
R12 Storage
R7 SERVER ROOM
Centre of floor · keeps all desks <90m
LOGICAL TOPOLOGY
INTERNET
R1
Cisco 2911 · NAT
CORE-SW1
L3 inter-VLAN · ACLs · SVI gateways
ACC-SW1
North wing
ACC-SW2
South wing
Trunks: 802.1Q · native VLAN 99 (black-hole)
QVIS · Olumide Akomolafe · Conestoga Network Support Technician
5 / 23

## Slide 6
EPISODE 02 · COMING UP
Building it in Packet Tracer
VLANs · trunks · inter-VLAN routing on the L3 core · named extended ACLs
~5 minutes · Cisco IOS configs walked line-by-line
6 / 23

## Slide 7
EP 02
VLAN PLAN
Segment by sensitivity, not by department label.
Ten VLANs · /24 each · gateway .1 on every SVI · pool .20-.199 · native VLAN 99 is the black-hole.
VLAN | Name | Subnet | Purpose
10 | MGMT | 10.10.10.0/24 | Network device management
20 | SERVERS | 10.10.20.0/24 | DC1 · DC2 · FS1
30 | EXEC-FIN | 10.10.30.0/24 | Executive + Finance + HR — most restricted
40 | STAFF | 10.10.40.0/24 | Sales · Marketing · Admin
50 | TECH | 10.10.50.0/24 | IT — full east-west, audited
60 | LAB | 10.10.60.0/24 | Training Lab — one-way isolated
70 | VOICE | 10.10.70.0/24 | VoIP (auxiliary VLAN on access ports)
80 | PRINT | 10.10.80.0/24 | Printers + MFPs
90 | GUEST | 10.10.90.0/24 | Guest Wi-Fi — internet only
99 | BLACKHOLE | — | Native VLAN on every trunk · no SVI · no access port
QVIS · Olumide Akomolafe · Conestoga Network Support Technician
7 / 23

## Slide 8
EP 02
IP PLAN & ADDRESS BUDGET
Every user VLAN sized for 10× headroom.
Doubling headcount fits in the same /24. No re-IP for the first three years.
PER-VLAN RANGE LAYOUT
.1
Gateway (SVI on CORE-SW1)
.2 – .9
Static infra (relay targets, APs)
.10 – .19
Servers and printers (reservations)
.20 – .199
DHCP pool
.200 – .254
Reserved static / future growth
CRITICAL STATIC ASSIGNMENTS
DC1 (AD + DNS + DHCP)
10.10.20.10
DC2 (failover partner)
10.10.20.11
FS1 (file server)
10.10.20.12
CORE-SW1 mgmt
10.10.10.1
ACC-SW1 mgmt
10.10.10.2
ACC-SW2 mgmt
10.10.10.3
R1 inside interface
10.10.0.1/30
R1 ↔ CORE-SW1 routed P2P /30 · 10.10.0.0/30 · no spanning-tree, pure L3
QVIS · Olumide Akomolafe · Conestoga Network Support Technician
8 / 23

## Slide 9
EP 02
EAST-WEST POLICY MATRIX
Named extended ACLs on every SVI · inbound · log-on-deny.
TECH can reach everywhere (it has to). LAB and GUEST are one-way isolated. Everyone else hits servers via permit-list.
From → To | EXEC-FIN | STAFF | TECH | LAB | SERVERS | PRINT | GUEST | Internet
EXEC-FIN | ✓ | ✗ | ✗ | ✗ | permit-list | ✓ | ✗ | ✓
STAFF | ✗ | ✓ | ✗ | ✗ | permit-list | ✓ | ✗ | ✓
TECH | mgmt | mgmt | ✓ | ✓ | ✓ | ✓ | ✗ | ✓
LAB | ✗ | ✗ | ✗ | ✓ | ✗ | ✗ | ✗ | ✓
GUEST | ✗ | ✗ | ✗ | ✗ | ✗ | ✗ | ✓ | ✓
Permit-list to SERVERS = DNS, DHCP, Kerberos, LDAP/LDAPS, SMB, print. Anything else is denied with log.
Why this is the firewall — for a 10-person office an extended ACL on the L3 core IS the policy enforcement layer. No separate appliance needed at this stage.
9 / 23

## Slide 10
EPISODE 03 · COMING UP
Identity and services
Active Directory · function-first OUs · AGDLP · DHCP · DNS · GPOs
~5 minutes · Windows Server 2022 · PowerShell scripts that are idempotent
10 / 23

## Slide 11
EP 03
IDENTITY STRATEGY
Six decisions. None flashy. All defensible.
qvis.local · Windows Server 2022 · functional level 2016
DECISION | CHOICE | WHY
Forest design | Single forest, single domain qvis.local | Twenty users does not justify multi-domain
Domain controllers | DC1 + DC2 | DC2 also hosts NPS / RADIUS for Wi-Fi
FSMO placement | All five roles on DC1 | Documented seize-procedure on DC2
Functional level | 2016 forest + domain on 2022 servers | Future-proof, tooling-compatible
UPN suffix | user@qvis.local internally, user@qvistech.ca externally | Same pattern · no user confusion
Time | PDC emulator on DC1 → time.nist.gov | Kerberos working ≡ time hygiene
QVIS · Olumide Akomolafe · Conestoga Network Support Technician
11 / 23

## Slide 12
EP 03
OU DESIGN — FUNCTION FIRST
Shape OUs by what they do, not by which team they belong to.
GPOs target behaviour (USB block, screen lock) rather than departments. Computers move with users. One disabled-account hold-out at the top.
qvis.local
└── OU = QVIS
├── OU = _Disabled ← offboarded users / decommissioned PCs
├── OU = ServiceAccounts
├── OU = Users
│ ├── OU = Executive
│ ├── OU = Finance-HR
│ ├── OU = Sales-Marketing
│ ├── OU = Technical
│ │ ├── OU = Network
│ │ └── OU = Cloud-Sysadmin
│ └── OU = Support-Admin
├── OU = Computers
│ ├── OU = Workstations (mirrors departments)
│ ├── OU = Laptops
│ └── OU = Servers (FileServers, Application)
└── OU = Groups
├── OU = Security (Role-Based · Resource · Privileged)
└── OU = Distribution
QVIS · Olumide Akomolafe · Conestoga Network Support Technician
12 / 23

## Slide 13
EP 03
AGDLP GROUP NESTING
Accounts → Global (role) → Domain Local (resource) → Permission.
No user ever ACL'd directly. No global group ever ACL'd directly.
A
Account
olumide.akomolafe
G
Global (role)
G_Network_Engineers
DL
Domain Local (resource)
DL_Share_NetworkDocs_RW
P
Permission
NTFS Modify on \\FS1\NetworkDocs
Why it matters
When Renata joins as Cybersecurity Analyst, I add her to G_Network_Engineers once. She inherits every share, printer, and VPN profile bound to that role. No share-by-share ACL editing. No drift. No "I thought you removed access in 2023."
13 / 23

## Slide 14
EP 03
DHCP
DC1 primary, DC2 failover — hot-standby, 5% reserve, 1-hour MCLT.
ip helper-address on every SVI relays to both DCs. Lease 8 days normal, 4 hours for Guest and Lab.
SCOPE | RANGE | LEASE | NOTES
QVIS-EXEC-FIN | 10.10.30.20 – .199 | 8 days | Reserved .200+ for static
QVIS-STAFF | 10.10.40.20 – .199 | 8 days | —
QVIS-TECH | 10.10.50.20 – .199 | 8 days | —
QVIS-LAB | 10.10.60.50 – .150 | 4 hours | DNS handed out = DC1 only
QVIS-VOICE | 10.10.70.20 – .199 | 8 days | Option 150 → TFTP for phones
QVIS-PRINT | 10.10.80.20 – .49 | 8 days | Reservations only
QVIS-GUEST | 10.10.90.20 – .254 | 4 hours | DNS = 1.1.1.1 / 9.9.9.9 (no internal resolver)
QVIS · Olumide Akomolafe · Conestoga Network Support Technician
14 / 23

## Slide 15
EP 03
DNS
AD-integrated · secure dynamic update only · forwarders fail closed.
One reverse zone covers the whole /16 internal range. Scavenging on.
FORWARD ZONE
qvis.local
AD-integrated
Secure dynamic update only
Replicates to every DC
Aging: 7d no-refresh + 7d refresh
REVERSE ZONE
10.10.in-addr.arpa
Covers entire /16 internal
Single zone (no per-/24 sprawl)
PTR records for static infra
Auto-PTR on AD-joined hosts
FORWARDERS
1.1.1.1 (Cloudflare)
9.9.9.9 (Quad9 – malicious-domain filter)
Root hints DISABLED
→ fails closed if forwarders down
5-second per-server timeout
QVIS · Olumide Akomolafe · Conestoga Network Support Technician
15 / 23

## Slide 16
EP 03
BASELINE GROUP POLICIES
Six GPOs. Each targets behaviour, not departments.
One link per policy. WMI filters where the policy is computer-WMI conditional.
GPO | LINKED TO | EFFECT
GPO_Baseline_AllUsers | OU=Users | 12-char password complexity · screen lock 10 min · lockout 5/15
GPO_Baseline_AllComputers | OU=Computers | Firewall on · BitLocker required · SmartScreen · WSUS
GPO_FinanceHR_USB_Block | OU=Users/Finance-HR + Executive | Removable storage read/write denied for USBSTOR
GPO_Mapped_Drives | OU=Users | M: \\FS1\Shared · U: \\FS1\Users\%username% · dept drives
GPO_Helpdesk_LocalAdmin | OU=Computers/Workstations | LAPS · G_Helpdesk_T1 in local Admins via Restricted Groups
GPO_Lab_Lockdown | OU=Computers/Workstations (WMI lab) | No corp drives · lab wallpaper · auto-logoff 18:00
QVIS · Olumide Akomolafe · Conestoga Network Support Technician
16 / 23

## Slide 17
EPISODE 04 · COMING UP
Troubleshoot like a technician
Three real tickets · OSI-shaped triage · root cause · runbook change
~5 minutes · the part hiring managers actually care about
17 / 23

## Slide 18
EP 04
STRUCTURED TRIAGE — OSI-SHAPED
Cheapest checks first. Up the stack methodically.
No guessing. No "I rebooted it." The value is the *method*, not the fix.
L7
Application
nslookup · curl · application logs
L6
Presentation
(rarely the cause)
L5
Session
auth state · session tokens · TLS handshake
L4
Transport
telnet / nc · firewall rules · ACL hits
L3
Network
ping · traceroute · routing table · NAT
L2
Data Link
show interfaces status · MAC · VLAN · trunk
L1
Physical
link light · cable · err-disabled
Start at L1. Stop the moment a check disconfirms an assumption — that's where the bug lives.
QVIS · Olumide Akomolafe · Conestoga Network Support Technician
18 / 23

## Slide 19
EP 04
CASE 1 · PORT-SECURITY ERR-DISABLE
"My new sales rep's PC has no network."
SYMPTOM
Liam, new sales rep. Plugged into R4 (bullpen). PC and phone on same cable both dead.
TRIAGE — UP THE STACK
L1 — link light on switch port and NIC
L2 — show interfaces status
L2 — show interfaces status err-disabled
L3 — ipconfig /all → ping gateway
ROOT CAUSE
Port came up err-disabled with reason psecure-violation. Liam plugged in a personal USB-Wi-Fi dongle. Phone (MAC 1) + PC NIC (MAC 2) + dongle (MAC 3) tripped the maximum-2 rule. Violation action shutdown closed the port.
FIX
ACC-SW1#
configure terminal
interface Fa0/11
shutdown
no shutdown
end
write memory
PREVENTION (RUNBOOK CHANGE)
Port-security did its job. Add to onboarding pack: corporate Wi-Fi only, no personal USB-NICs. If this becomes frequent, consider violation restrict.
19 / 23

## Slide 20
EP 04
CASE 2 · ACL ORDERING MISTAKE
"All of Sales lost the file server at 11 a.m."
SYMPTOM
Every Sales PC has internet but can't reach \\FS1\sales. EXEC-FIN and TECH are fine.
TRIAGE — UP THE STACK
L3 — ping gateway from Sales PC: OK
L3 — ping FS1 from Sales PC: FAILS
L3 — ping FS1 from CORE-SW1: OK
L4/Policy — show access-lists ACL-STAFF-IN
ROOT CAUSE
The senior network engineer was hardening ACL-STAFF-IN that morning and pasted the deny-RFC1918 catch-all before the SMB permit lines. ACLs match top-down, first hit wins. Sales → SERVERS hit the deny first.
FIX
CORE-SW1(config)# ip access-list extended ACL-STAFF-IN
no 60
200 deny ip 10.10.40.0 0.0.0.255 10.10.30.0 0.0.0.255 log
PREVENTION (RUNBOOK CHANGE)
ACL changes go through peer review with explicit sequence numbers. Hit-count alarm on any deny+log line that suddenly starts incrementing.
20 / 23

## Slide 21
EP 04
CASE 3 · DNS · ACL · DHCP MISALIGNMENT
"DNS works for everyone except the Training Lab."
SYMPTOM
Lab PCs on VLAN 60 get DHCP, can ping 8.8.8.8, but nslookup google.com times out.
TRIAGE — UP THE STACK
nslookup google.com 10.10.20.10 → timeout (DC1)
nslookup google.com 1.1.1.1 → answers (Cloudflare)
ping 10.10.20.10 → timeout
show access-lists ACL-LAB-IN
ROOT CAUSE
ACL-LAB-IN permits DNS only to DC1 (10.10.20.10), not DC2. But the lab DHCP scope was handing out BOTH DCs. Clients trying DC2 timed out; Windows would fall back to DC1 after several seconds — which is the timeout the users were reporting.
FIX
Set-DhcpServerv4OptionValue
-ScopeId 10.10.60.0
-DnsServer 10.10.20.10
PREVENTION (RUNBOOK CHANGE)
ACL and DHCP changes share one change document. Synthetic monitor hits both DCs from the lab VLAN every hour and pages on either failing.
21 / 23

## Slide 22
EP 04
WHAT THESE THREE HAVE IN COMMON
The fix is small. The triage is the value.
THE FIX
1. One toggle on a switch port
2. One ACL re-sequence
3. One DHCP option override
Every fix above is one or two lines. Nobody pays a technician for the line — they pay for finding it.
THE TRIAGE
1. Move methodically up the OSI stack
2. Cheapest checks first
3. Hit counts and err-disabled before guessing
Be willing to say "I haven't reproduced it yet" instead of pretending. That's the technician part.
Six cases total in the portfolio — three shown here, three more in the source repo (printer drift, GPO trust-relationship break, Wi-Fi RF saturation in the conference room).
QVIS · Olumide Akomolafe · Conestoga Network Support Technician
22 / 23

## Slide 23
THANKS FOR WATCHING
I'm available.
Looking for Tier-1 / Tier-2 Network Support roles in Ontario.
EMAIL
oakomolafe404@gmail.com
LINKEDIN
https://www.linkedin.com/in/olumide-akomolafe-818311391/
LOCATION
Cambridge, Ontario · willing to commute KW + Toronto
SOURCE REPO
https://github.com/meeeiii
Tell me what you'd want me to build next.
23 / 23